## Slide 1: Long-Term Sustainability of Behavior Change due to CHCs
Masters Dissertation for Louis Tobergte
University of Leeds
In-Country Research Assistant: Andrew Muringaniza, Africa AHEAD Program Manager
Presented by Nigel Stuart, Africa AHEAD Side Event, UNC Conference, USA
October 30th, 2015

## Slide 2: Content
Introduction
Methodology
Zimbabwe Situation
Sanitation Changes
Hygiene Changes
Key Informant Interviews
Recommendations
Conclusion

## Slide 3: Introduction
Demand-creation methodologies central to SDG success
  CHCs and CLTS in use in over 50 countries combined
Immediate impact well-researched
Long-term impact largely unknown
  Plan International CLTS study: 21% slippage rate on latrine use in 2-3 years
  CHCs: no longitudinal studies done
    Only one published independent study (Whaley and Webster, 2011)
Purpose of this research:
  Analyze the long-term sustainability of CHC-inspired WaSH behavior changes
  Produce an independent study
  Provide recommendations to Africa AHEAD to improve their methodology

## Slide 4: 2013 Plan International CLTS Results
21% no longer with a clean and/or functioning latrine
92% did not meet the original ODF criteria
5 original ODF criteria
Functioning latrine with superstructure
Means of keeping flies from the pit
Absence of excreta in vicinity of the house
HWF with soap/ash
Evidence of latrine and HWF use
Tyndal-Biscoe, et al, 2013
Notes: The red line represents the average of the whole study and is the only important line in the graph.
The line climbs as more and more of the original 5 ODF criteria were applied to the households. It starts with the most basic criterion – presence of a functioning latrine, and then adds more and more of the criteria until you reach the top right, where only 8% of survey respondents had a clean, functioning latrine with a lid over the hole and a hand-washing facility with soap or ash and evidence of their use.

## Slide 5: Methodology
Household surveys with verifiable and self-reported proxy indicators
  6 CHC villages surveyed 5 years since last contact with Africa AHEAD
    7 years post-PHHE portion (completed in 2007/08)
    5 years post-FAN phase (completed in 2010)
    105 CHC graduates – completed all 20 PHHE lessons
    32 non-graduates – completed 0 to 8 lessons
  2 non-CHC villages surveyed
    No WaSH-related programs
    As similar as possible to CHC villages (location, wealth, etc)
    45 households
  Survey based on Plan International’s survey
    Focused on WaSH behaviors pre-CHC and at time of study
    Latrine and HWF use verified by research team
  Statistical Analysis: Chi-squared tests with an α-value of 0.05
23 key informant interviews
    Village Heads and Village Health Workers
    Nurse Aids at clinics, Ward Councilors, and Africa AHEAD staff
Notes: The villages completed the PHHE portion over 7 years before the study.
2 districts were surveyed, with the study locations starred on the map on the next slide. In each district, 3 CHC and 1 non-CHC village were surveyed. The CHC village surveys included both graduates and non-graduates.
The non-CHC villages were neighboring villages, but the respondents were questioned to ensure that there was not significant ‘spillover’ from the nearby CHC villages.

## Slide 6: Constraints
Sample size: only 182 households total
  8 villages total, between 12% and 50% of households in a village surveyed
  18-32 surveyed per village
Lack of baseline data: pre-CHC data relied upon memory of respondents
  Effect mitigated by presence of Community-Based Facilitators who verified the responses
Social desirability bias: biggest impact on reports of practicing CatSan and handwashing
  CBFs understood importance of accurate responses and helped ensure honest answers from respondents
Influence of other programs: some health education at clinics
  Village Heads and Village Health Workers reported no programs since CHC

## Slide 7: Zimbabwe’s Situation
Buhera District
Chipinge District
Overview
2008: hyperinflation
  Switch to US $
85% unemployment
3 million people fled
Very low incomes in rural areas (Whaley and Webster, 2011)
Many rural civil servants underpaid or not paid
  Village Health Workers
  Environmental Health Technicians
Notes: The areas surveyed in Buhera and Chipinge were both dominated by subsistence agriculture. There were a few people employed as shopkeepers as well. Both areas depended upon seasonal rains for their crops and had poor harvests the year before the study.

## Slide 8: Rural Sanitation Picture
From 1995 to 2012
Improved: -3%
Shared: -2%
Other unimproved: +11%
OD: -6%
Trends
General dilapidation of infrastructure
Rise of temporary pit latrines
Slow decrease in OD

## Slide 9: Villages
Villages from 34 to 200 households
Participation rates varied from 53% to 125%
One village had 1.25 graduates per household
Notes: The first 4 villages were from Chipinge, and the last 4 were from Buhera. All of the villages were located nearby each other, and though they were not given an advance warning of our arrival, some houses knew we were coming because word had spread. However, this had little impact on the study, because it was very obvious if someone had recently built either a latrine or HWF.

## Slide 10: Sanitation Changes
Baseline Toilet Coverage:
47% vs 39%, p > 0.1
2015 Toilet Coverage
60% vs 35%, p < 0.001
Amongst CHC grads, toilet use increased by 13%, while use decreased by 4% amongst non-graduates.
OD/CS of CHC grads dropped by 14%, compared to an 11% increase amongst non-graduates.
Research team suspected that many reports of CatSan were false
- Based on VHW testimony
Chart: 
| Pre-CHC | Current | Pre-2010 | Current | CHC Graduates (105) |  | Non-Graduates (77)
Toilet Present (with evidence of use) | 0.47 | 0.6 | 0.39 | 0.35065
Other | 0.043796 | 0.052381 | 0.0773 | 0.0096104
Cat Sanitation | 0.085714 | 0.24762 | 0.0827 | 0.25974
Adjusted OD | 0.4 | 0.1 | 0.45 | 0.38
White Fill | 1
OD
Toilet
CatSan
Other
Notes: ‘Toilet’ included any sort of fixed-point defecation method with a superstructure – the three types were VIPs, Pit latrines, and temporary pit latrines. There also had to be evidence of the toilet’s use (well-trodden path, ash strewn in pit, etc)
If a latrine was present but clearly not in use, the house was counted as OD. This only happened 5 times throughout the study.
Cat sanitation was unverifiable, but it does at least hint at the better knowledge of proper sanitation by respondents.
‘Other’ includes people using neighbor’s or public latrines.
The one discrepancy between the comparisons is that the non-CHC villages were asked about pre-2010 sanitation practices, while CHC villagers were asked about pre-CHC practices. But, this would only have altered 2-3 houses and lowered the ‘pre’ levels by a few percentage points (3-4%) down to 35%, and does not affect the statistical significance results reported below.
Amongst graduates, Toilet use increased by 13%, while use decreased by 4% amongst non-graduates. Similarly, the of OD/CS of graduates dropped by 14%, compared to an 11% increase amongst non-graduates.
Differences in baseline levels of toilet coverage were not statistically significant (p>0.1)
Toilet coverage at the time of the study was significantly different between the two groups, (60% vs 35%, p<0.001)

## Slide 11: Changes within CHC Villages
Chart: 
| Pre-CHC | Current | Pre-CHC | Current | CHC Graduates (105) |  | Non-Grads from CHC Villages (32)
Toilet Present (with evidence of use) | 0.46667 | 0.6 | 0.53 | 0.375
Other | 0.043796 | 0.057143 | 0.0325 | 0
Cat Sanitation | 0.085714 | 0.24762 | 0.15625 | 0.34375
Adjusted OD | 0.4 | 0.095238 | 0.28125 | 0.28125
OD
CatSan
Other
Toilet
CHC grads: 13% increase in past 7 years
Non-grads: 15% decrease in past 7 years
Non-grads left behind
Presence of CHC in a village not enough to influence behavior significantly
Notes: The households that did not have a CHC graduate were completely left behind on sanitation progress, regressing significantly.
The only partial explanation is that Non-grads from CHC villages had a much lower repair/rebuild rate, at 25% compared to 59% for the CHC graduates, though this was not statistically significant (p=0.058). Why they had such a low repair rate is unknown though.
More research needs to be done on why this happened, but the CHC program needs to improve on inclusiveness of non-graduates, perhaps even putting some emphasis on the ‘total sanitation’ of a village, similar to the CLTS focus on 100% coverage.

## Slide 12: Sanitation Resiliency
Chart: 
| % of houses with collapse, fill up, or moved | % of collapses repaired/rebuilt | % of houses improving Sanitation since CHC
CHC Graduates | 0.42 | 0.59 | 0.23
Non-Grads | 0.39 | 0.36 | 0.1
p = 0.058
p < 0.05
59% of collapses amongst CHC grads were rebuilt or repaired since the CHC without external support
- 23% higher than non-grads (p=0.058).
Sanitation improvements: upgrading latrine, adding a roof/vent pipe, moving from OD/CS to a latrine, etc.
Notes: The collapse rate (includes collapses, fill ups and house-movings) was similar for all groups, about 40%.
Repair rates were very different, but not statistically significantly (59% vs 36%, p=0.058)
The percentage of houses improving their sanitation since the end of the CHC (2010) was significantly higher amongst CHC graduates (23% vs 10%, p<0.05)

## Slide 13: Latrine Types
Chart: 
| CHC Graduates (67) | Non-Graduates (31)
VIP | 0.41791 | 0.51613
Pit | 0.37313 | 0.096774
Temporary Pit | 0.20896 | 0.3871
Temporary Pit
Temporary Pit
Pit
VIPs
CHC graduates built more permanent latrines on the whole
Notes: The breakdown of latrine types shows that CHC graduates built more permanent latrines on the whole, but, this graph hides a lot of intricacies shown in the next slide.

## Slide 14: Latrine Type by District and Program
Chart: 
| CHC Grads (32) | Non-Grads (15) | CHC Grads (42) | Non-Grads (16) | Buhera |  | Chipinge
VIP | 0.72 | 0.93333 | 0.2381 | 0.125
Pit | 0.24 | 0 | 0.45238 | 0.1875
Temporary Pit | 0.04 | 0.066667 | 0.30952 | 0.6875
Temporary Pit
45%
Temporary Pit
Pit
VIPs
12%
In Buhera, temporary latrines were very rare compared to in Chipinge where they were more common
Notes: Latrine materials varied significantly by district.
In Buhera, temporary latrines were very rare, while in Chipinge, almost half of latrines were temporary pit latrines. It seems that the Buhera villages did not buy into trying temporary latrines as a first step towards better sanitation.
It is suspected that because Buhera compounds almost always included more than one concrete structure, those people were unwilling to put up a structure that would look ‘out of place’ in their compound. Meanwhile, in Chipinge, many people still had pole-and-dagga huts, and thus temporary latrines fit in well.

## Slide 15: Sex of Head of Household and Latrine Ownership
Chart: 
| CHC Graduates | Non-Grads
Male-Headed Households | 0.583 | 0.41169
Female-Headed Households | 0.697 | 0.31338
CHC program seems to have affected women’s self-efficacy in regards to sanitation.
Grads: female-headed households had 12% higher latrine coverage than male-headed
Non-grads: female-headed households had 10% lower coverage
Notes: Amongst CHC graduates, female-headed households were actually more likely to own a latrine than male-headed households, though it was not a statistically significant difference (70% vs 58%, p=0.25).
However, when compared to non-graduate male-headed households having a higher ownership rate, this finding suggests that the CHC program did have some effect on women’s self-efficacy in regards to sanitation. It also suggests that having a decision-maker enroll in the program can lead to more change, as women made up most of the club membership.

## Slide 16: Select Sanitation and Hygiene Indicators
Chart: 
| Full 4 Handwashing | Reported HW w/ Soap/ash after Toilet | Reported HW w/ Soap/ash Today | Reported no HW w/ Soap/ash in last week | % of Latrines with Fly Barrier | Reported Field OD | Reported diarrhea in last 2 weeks
CHC Graduates (n = 105) | 0.1 | 0.82 | 0.68 | 0.11 | 0.089552 | 0.057143 | 0.17
Non-Grads (n = 77) | 0 | 0.62195 | 0.4326 | 0.27481 | 0.034632 | 0.24675 | 0.26442
p = 0.14
p < 0.005
p < 0.0005
“People will [..] build a very nice toilet with a vent pipe, but they don’t put a fly screen. And then [I’ll] say, ‘Why?’ And they’ll say that. ‘It’s more important to have your feces down in the hole.’ - VHW
Notes: ‘Full 4 HW’ refers to a household meeting the following 4 criteria:
HWF present
Water present
Soap/ash present
Evidence of recent use
Graduates significantly outperformed non-graduates on Full 4 HW at 10% vs 0%, p<0.005.
The next three columns show comparisons of non-verifiable data: how many households reported washing their hands with soap/ash after using the toilet, on the day of the survey, and not in the last week at all. At the least, these results show that graduates had a better knowledge of what HW behaviors were desirable.
The percentage of latrines with fly barriers was low all-around at 9% of grads and 3% of non-grads, marking another area needing improvement.
Reported OD while working in the fields was significantly lower amongst CHC graduates, but was similarly unverifiable by the research team (6% vs 25%, p<0.0005).
Reported diarrhea in the last 2 weeks was higher amongst non-graduates, but not significantly so (17% vs 26%, p=0.14).

## Slide 17: Diarrhea
Interviewees consistently claimed lower diarrhea rates due to the CHC
  2 veteran nurse aids estimated over a 40% decrease in diarrhea due to the CHC
“There was a decrease of patients coming to the clinic because they know how to treat it at home, unlike before where one would simply rush to the clinic after very little time with the running stomach.” Buhera Nurse Aid

## Slide 18: Motivation Analysis
Across all respondents, health was by far the most commonly reported motivator
  Conflicts strongly with Curtis view and supports Waterkeyn PhD research
Possibly due in part to the historically high literacy and education rates in Zimbabwe
Also could be due to the health-focused messaging of the CHC program
Shame/disgust was almost non-existent as a response
Curtis, et al, 2009
Waterkeyns, 2013

## Slide 19: Education
Less educated households much less likely to have a CHC member
  p < 0.005
Many less-educated households did graduate
Notes: Possible perception problem - What do you mean here?

## Slide 20: Village Cohesiveness
All VHWs and VHs reported stronger cohesiveness since the CHC
“[Cohesiveness] has strengthened since the CHC because they’ve continued meeting since then.” – Village Head
“In the garden there is a portion set aside for such [vulnerable] people and they always send vegetables out to the elderly.” - VHW
However, cohesiveness did not extend to caring for vulnerable households’ sanitation needs
“There is no cohesiveness on the construction of latrines.” – Village Head
“That [helping vulnerable households construct latrines] could be a new idea because we had never thought about it… So far, each person is building his individual [latrine].” - VHW

## Slide 21: Politicization
In Buhera, some clubs became meeting places for political activities
Opposing party members would stop attending
These clubs had low attendance and little effect on health of the community
  Did provide a space for citizens to meet and band together
Village 7: politicized club
  Only 53% participation
  Decrease in toilet coverage
Chart: 
| Pre- CHC | 2015 | Village 7 (n = 18)
Toilet Present (with evidence of use) | 0.5 | 0.44
Other | 0 | 0
Cat Sanitation | 0.06 | 0.17
OD (Adjusted) | 0.44 | 0.39

## Slide 22: High level of Club Sustainability
85% of CHC graduates still involved with the club five years after FAN phase
All villages had at least one functioning community garden
  Gardens only abandoned if water point failed
  Due to a drought prior to the research, these gardens were often the only source of food/income for the villages throughout the fieldwork

## Slide 23: Recommendations
Follow-up visits to capitalize on Club sustainability
  Bring new lessons to help re-invigorate the club
  Shows members that Africa AHEAD still cares about them – in turn, motivates them to show Africa AHEAD that they still practice the lessons
  Important to have an outsider come teach/inspect: elicits a greater response from the villagers
Sanitation hardware lessons
  Increase male involvement in program
  Improve households’ abilities to construct latrines and hold masons accountable
Sanitation plans
  Already in place to some degree
  Ensure it includes vulnerable and non-CHC households
Use CBFs and Village Heads to reach out to vulnerable groups, particularly the less-educated

## Slide 24: Conclusion
CHCs left a definite and sustainable impact even after 5 -7 years
  Sanitation: sizeable improvement, but could be better
  Handwashing: some improvement, needs more reinforcement
  Club infrastructure sustainable, particularly with nutrition gardens
Small changes to the methodology could lead to huge improvements in sustainability
  Less-educated households and elderly households need to be actively encouraged to join

## Slide 25: Acknowledgments
Barbara Evans: Dissertation supervisor and primary motivator
Juliet Waterkeyn (Africa AHEAD, CEO) : Supporting the research
Andrew Muringaniza (Africa AHEAD, Programme Manager): Invaluable guide & interpreter
Zimbabweans in project areas: Graciously answered my many questions
References
Curtis, V. et al. 2009. Planned, motivated and habitual hygiene behavior: an eleven country review. Health Education Research 24(4), pp. 655-73.
Tyndale-Biscoe, P. et al. 2013. ODF Sustainability Study.
Waterkeyn, J & Waterkeyn A. Creating a culture of health: hygiene behaviour change in community health clubs through knowledge and positive peer pressure. Journal of Water, Sanitation and Hygiene for Development Vol 3 No 2. 144–155.
Whaley, L. and Webster, J. 2011. The effectiveness and sustainability of two demand driven sanitation and hygiene approaches in Zimbabwe. Journal of Water, Sanitation and Hygiene for Development 1(1), pp.20-36.

## Slide 26: Contact Info
Louis Tobergte
2nd Lieutenant, Engineer Officer in the US Army
Email: Louis.tobergte@gmail.com
Cell: +1(573) 855-3611
Skype: ltobergte2
Send me any questions you have! Apologies for not making it today.
*The opinions expressed do not necessarily represent those of the Department of the Army, the Department of Defense, or the Government of the United States.